## Slide 1: Forces Objects can affect other objects at a distance and changing the movement of an object requires a net force to be acting upon it.

## Slide 2
The Big Investigation
Investigate the effect of varying force (with constant mass) and then varying mass (with constant force) on an object on its acceleration.

## Slide 3: Stopping a moving car
Today I will be able to describe the motion of an object from a velocity/time graph.
I will be able to calculate acceleration and distance using a velocity/time graph
Draw a free body diagram of a car stopping. Label all the forces (remember magnitude is the length of the force arrow) acting on it and the resultant (if any) force.

## Slide 4: Lesson Outcomes
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these
Success Criteria:
Define Stopping distance as thinking plus braking distance
Analyse factors that will affect these
Apply knowledge to solve problems relating to stopping distances.

## Slide 5: Stopping distance
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these
What does this mean?
THINK
PAIR
SHARE
2 minutes!

## Slide 6: Stopping distances


Thinking distance is the distance a car travels before the brakes are applied.
Braking distance is the distance a car travels whilst the brakes are being applied.
Stopping distance = thinking distance + braking distance
Stopping distance
Braking distance
Thinking distance
How long does it take a moving vehicle to stop?
The stopping distance is the sum of the thinking distance and the braking distance.

## Slide 7: Braking distance
The distance the car travels during its deceleration, whilst the brakes are being applied
The distance the car travels in the split second between a hazard appearing and the driver applying the brakes
Thinking distance

## Slide 8
The total stopping distance = thinking distance + braking distance
30mph
9m +
14m = 6 car lengths
50mph
15m + 38m = 13 car lengths
70mph
21m + 75m = 24 car lengths

## Slide 9: Thinking distance
What is going to affect the thinking distance of a driver?
Think
Pair
Share
2 mins
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these

## Slide 10: Thinking distance
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these
How fast you are going – the faster you are going the more distance you will go while you are reacting to a hazard
Your reaction time – how fast you respond to hazards.
  This can be affected by;
  Tiredness
  Alcohol or drugs
  Lack of concentration – phones/texting/changing music
  A typical reaction time is between 0.2 and 0.9 seconds.

## Slide 11: Braking distance
What is going to affect the braking distance of a car?
Think
Pair
Share
2 mins
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these

## Slide 12: Braking distance
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these
How fast you are going – the faster you go the more distance it takes to stop
How good your brakes are – worn or faulty brakes will not apply as much force as good, well maintained brakes and could fail in an emergency
How good the tyres are – tyres need a minimum tread depth of 1.6mm. This helps in wet conditions to disperse surface water away from the contact are between tyre and road.
Weather conditions – hot dry days will increase the friction between tyre and road, wet or icy conditions will decrease the friction leading to longer braking distances

## Slide 13: Speed and stopping distance
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these
If a cars speed doubles, thinking distance will double.
If a cars speed doubles, braking distance increases four fold (22).
If a cars speed trebles, braking distance increases nine fold (32)
So we can say braking distance increases with the square of the scale factor of the speed increase.

## Slide 14: Speed and braking distance
Using your previous knowledge can you explain why speed affects braking distance this way?
HINT – it’s a transfer of energy
KE of vehicle = so if v doubles KE increases four fold
KE = Work done = Fs and F is the braking force which is constant so s must also increase four fold
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these

## Slide 15: Worked example
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these

## Slide 16: Your turn
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these

## Slide 17: Your turn
Today I will be able to define stopping distance, thinking distance and braking distance and discuss factors affecting these